1. Configure OSPF process id 1 on R6, R7, and R9
  1. R6 & R7 : do not use any interface-level commands.
  2. R6 : enable OSPF only for interfaces with exact IP of Lo0 and eth0/1.67.
  3. R7 : enable OSPF on all interface with the subnets of Eth0/1.67 and Eth0/1.79.
  4. R9 : Use only interface-level commands
  5. Area 67 between R6 and R7, and Loopback0 of R6 and R7.
  6. Area 79 between R7 and R9, and Loopback0 of R9.
  7. Ensure R7 has connectivity with R6 and R9’s Loopback0.
  8. Why R6 and R9 doesn’t receive any OSPF routes ?
  9. Configure R7 so R6 and R9 receive inter area OSPF routes
2. Configure OSPF process id 1 area 0 on R1, R2, R3, R4, and R5
  1. advertise lo0 prefixes of R1 – R2 into area 0
  2. advertise lo0 prefixes of R3 – R4 into area Y, Y is the router number
  3. Use single network command on R5.
  4. Use only interface-level on DMVPN spokes.
  5. Change default OSPF network type to non-broadcast
  6. Ensure IP connectivity between loopback0 prefixes of the routers